## Slide 1: INTRODUCTION TO COMPUTER ARCHITECTURE AND ASSEMBLY LANGUAGE

## Slide 2
Learning outcomes:
Define Computer Architecture: Students will be able to define the term "computer architecture" and explain its significance in understanding the organization of computer systems.
Identify Key Components: Students will be able to identify and describe the main components of a computer system, including the Central Processing Unit (CPU), memory, and Input/Output (I/O) devices.
Differentiate Instruction Set Architectures: Students will be able to differentiate between different types of Instruction Set Architectures (ISAs), such as Complex Instruction Set Computer (CISC) and Reduced Instruction Set Computer (RISC).
Determine performance: Students will be able to calculate performance based on execution time with a given instruction count, clock rate, and CPI.

## Slide 3
Computer
Processor (CPU)
Computer
Control
(“brain”)
Datapath
(“brawn”)
Memory
(passive)
(where
programs,
& data
live when
running)
Devices
Input
Output
Display, Printer
Keyboard, Mouse
Disk (where
programs,
& data
live when
not running)
The components of every computer, past and present, belong to one of these five categories, and are connected by bus
Data from the outside world to the computer
These data are kept in the memory until ...
Datapath request and process them
The operation is controlled by Control Unit
Processed data back to the outside world
Computer

## Slide 4
Rapidly changing field:
  Vacuum tube  Transistor  IC  VLSI SoC
  Doubling every 1.5 years (Moore’s Law):
    memory capacity
    processor speed (due to advances in technology and hardware)
  Funny example: if Boeing had kept up with IBM we could fly from KLIA to NY in 10 minutes by 10 RM !!
Things we’ll be learning:
  how computers work, what’s a good design, what’s not
  Assembly Language Programming
  issues affecting modern processors (e.g., caches, pipelines)
Introduction

## Slide 5
Our Focus
CPU consists of
  datapath
  control
…implemented using millions of transistors
…impossible to understand by looking at individual transistors
we need...

## Slide 6
Abstraction
Delving into the depths reveals more information, but…
An abstraction omits ‘un-wanted’ detail, helps us cope with complexity
From the figure on the right, how does abstraction help the programmer and how does he/she avoid too much detail?

## Slide 7
Instruction Set Architecture
instruction set
software
hardware

## Slide 8
Instruction Set Architecture
A very important abstraction:
  interface between hardware and low-level software
  standardizes instructions, machine language bit patterns, etc.
  advantage: allows different implementations of the same architecture
  disadvantage: sometimes prevents adding new innovations
Modern instruction set architectures:
  80x86/Pentium/K6, PowerPC, DEC Alpha, MIPS, SPARC, HP, Motorola

## Slide 9
Instruction Set Architecture
Instruction Set Architecture (ISA) is a crucial aspect of computer architecture, defining the set of instructions that a CPU can execute and the format of these instructions. Different computer architectures have distinct ISAs, which influence how software interacts with hardware. Here, we'll differentiate between two common types of ISAs: Complex Instruction Set Computer (CISC) and Reduced Instruction Set Computer (RISC).
It's important to note that modern CPUs often incorporate elements of both CISC and RISC architectures, blurring the lines between the two. For example, x86 CPUs, which have a CISC heritage, use microcode to translate complex instructions into simpler micro-operations (micro-ops) that are executed in a more RISC-like fashion.
Ultimately, the choice between CISC and RISC architecture depends on factors such as performance requirements, energy efficiency, and compatibility with existing software and hardware standards. Some processors, like ARM, are known for their RISC-based designs, while others, like Intel and AMD x86 processors, incorporate elements of both CISC and RISC to balance performance and compatibility.

## Slide 10
Instruction Set Architecture - CISC
Complex Instruction Set Computer (CISC):
Instruction Complexity: CISC architectures feature a wide range of complex instructions that can perform multiple tasks in a single instruction. These instructions are typically variable in length.
Microcode: CISC CPUs often use microcode to implement complex instructions. Microcode is a lower-level set of instructions used by the CPU to execute the higher-level CISC instructions.
Memory Access: CISC architectures tend to rely on memory-based addressing modes, allowing instructions to operate directly on memory locations. This can result in fewer instructions per program but more complex instructions.
Pipeline Stages: CISC CPUs may have longer instruction pipelines due to the complexity of their instructions. This can lead to a slower clock speed but potentially fewer instructions per program.
Code Density: CISC instructions tend to be more memory-intensive due to their complexity, potentially leading to larger program sizes.
Legacy Support: Many older computer architectures, such as the x86 architecture, are CISC-based. They maintain backward compatibility with earlier generations, which can result in complex and sometimes inefficient instruction sets.

## Slide 11
Instruction Set Architecture - RISC
Reduced Instruction Set Computer (RISC):
Instruction Simplicity: RISC architectures have a smaller and more simplified set of instructions, with a focus on performing basic operations efficiently. Instructions are typically of fixed length.
No Microcode: RISC CPUs typically avoid microcode, relying on hardwired control units for instruction execution.
Load/Store Architecture: RISC architectures follow a load/store model, meaning that only load and store instructions can access memory directly. All other operations must use registers, promoting register-based data manipulation.
Shorter Pipeline: RISC CPUs often have shorter instruction pipelines, allowing for faster clock speeds and reduced latency. However, this can lead to potentially more instructions per program.
Code Density: RISC instructions tend to be more compact, resulting in smaller program sizes and more efficient memory usage.
Efficiency and Performance: RISC architectures prioritize the efficient execution of simple instructions, making them well-suited for high-performance computing and pipelining.
Simplified Addressing Modes: RISC architectures typically have fewer addressing modes, simplifying the instruction set and reducing complexity.

## Slide 12
What is Computer Architecture?
Computer Architecture =
Instruction Set Architecture +
Machine Organization

## Slide 13
What is Computer Architecture?
I/O system
Instruction Set Proc.
Compiler
Operating
System
Application
Digital Design
Circuit Design
Instruction Set
Architecture
Firmware
Datapath & Control
Layout
HLL

## Slide 14
Computer Architecture
Computer architecture refers to the design and organization of the various components that make up a computer system. It encompasses both the hardware and software aspects of a computer and defines how they interact to perform computational tasks. Computer architecture involves making decisions about the organization and functionality of a computer's central processing unit (CPU), memory hierarchy, input/output subsystems, and other critical components.
Key aspects of computer architecture include:
Instruction Set Architecture (ISA): This defines the set of instructions that a CPU can execute and the format of these instructions. The ISA serves as the interface between software and hardware, allowing software programs to communicate with and control the hardware.
Memory Hierarchy: Computer architects design memory systems that include various levels of storage, such as registers, caches, main memory, and secondary storage (e.g., hard drives or solid-state drives). The memory hierarchy is critical for managing data storage and access efficiently.
Central Processing Unit (CPU): The CPU is the heart of the computer, responsible for executing instructions from programs. Computer architects design CPUs to maximize performance, considering factors like instruction execution pipelines, clock speeds, and microarchitecture.

## Slide 15
Computer Architecture
Input/Output Systems: Computer architecture also includes the design of input and output systems, which allow data to be transferred between the computer and external devices (e.g., keyboards, displays, storage devices).
Interconnection and Bus Systems: Architects design the communication pathways (buses) that connect various components within the computer, ensuring data and control signals can flow between them efficiently.
Parallelism and Pipelining: Modern computer architectures often incorporate parallelism and instruction pipelining techniques to enhance performance, allowing multiple instructions to be executed simultaneously or in overlapping stages.
Power Efficiency: Energy efficiency is an increasingly important consideration in computer architecture, with architects striving to design systems that deliver high performance while minimizing power consumption.
Computer architects work to balance various design constraints, including performance, power efficiency, cost, and compatibility with existing software and hardware standards. They play a crucial role in shaping the capabilities and characteristics of computer systems, from personal computers and servers to mobile devices and embedded systems. Understanding computer architecture is essential for both hardware and software developers, as it provides insights into how computers execute instructions and manage data, which is vital for optimizing software performance and designing efficient hardware.

## Slide 16
Key Concepts of Computer Architecture
Computer architecture encompasses the design and organization of various components that make up a computer system. These components work together to execute instructions and process data. The key components of computer architecture include:
Central Processing Unit (CPU): The CPU is the core processing unit of a computer. It performs arithmetic and logical operations and executes program instructions. The CPU consists of several sub-components, including:
  Arithmetic Logic Unit (ALU): Responsible for performing mathematical and logical operations.
  Control Unit: Manages the execution of instructions, fetches instructions from memory, and decodes them.
  Registers: High-speed, small-capacity memory locations within the CPU for temporary data storage and manipulation.
Memory Hierarchy: Computer systems have a memory hierarchy that includes various levels of storage, each with different capacities, speeds, and costs. The memory hierarchy typically consists of:
  Registers: Fastest and smallest memory units, located within the CPU.
  Cache Memory: Faster than main memory but smaller in capacity. It serves as a buffer between the CPU and main memory.
  Main Memory (RAM): Provides larger storage capacity than cache and serves as a temporary workspace for program data and instructions.
  Secondary Storage: Slower than main memory but offers much greater capacity. Includes hard drives (HDDs), solid-state drives (SSDs), and other non-volatile storage devices.
  Tertiary Storage (optional): Used for long-term archival storage and backup, such as magnetic tapes or optical discs.

## Slide 17
Key Concepts of Computer Architecture
Input/Output (I/O) Subsystem: The I/O subsystem enables communication between the computer and external devices. Key components include:
  Input Devices: Such as keyboards, mice, and sensors, allow users to provide data and commands to the computer.
  Output Devices: Like displays, printers, and speakers, provide feedback and present results to users.
  I/O Controllers: Manage the flow of data between the CPU, memory, and I/O devices.
  Buses: Communication pathways that connect various components, including the CPU, memory, and I/O devices.
System Interconnect: The system interconnect includes buses and communication pathways that connect the CPU, memory, and I/O devices. It ensures data and control signals can flow between components efficiently.
Instruction Set Architecture (ISA): The ISA defines the set of instructions that the CPU can execute. It includes machine-level instructions specifying operations like arithmetic, logic, data movement, and control flow. The ISA serves as the interface between software and hardware.

## Slide 18
Key Concepts of Computer Architecture
Clock and Timing: The computer architecture includes a clock and timing system that synchronizes the operations of various components, ensuring proper coordination and sequencing of tasks.
Power Supply and Cooling: These components provide the necessary electrical power to run the computer while maintaining safe operating temperatures. Cooling systems, such as fans and heat sinks, dissipate excess heat generated by components.
Microarchitecture: The microarchitecture refers to the specific design and organization of the CPU's internal components, including its instruction pipeline, execution units, and memory hierarchy.
I/O Ports and Interfaces: These components facilitate the physical connection between the computer and external devices. They often include USB ports, audio jacks, network interfaces, and expansion slots.
Firmware and BIOS/UEFI: Firmware is software stored on non-volatile memory (e.g., BIOS or UEFI) that initializes the computer hardware during boot-up and provides low-level control and configuration options.
These key components collectively define the architecture of a computer system, determining its capabilities, performance, and functionality. Computer architects and engineers carefully design and optimize these components to achieve specific objectives, such as high performance, energy efficiency, or cost-effectiveness, depending on the intended use of the computer.

## Slide 19: Who Uses Assembly Language
The machine designer
  must implement and trade-off instruction functionality
The compiler writer
  must generate machine language from a HLL
The writer of time or space critical code
  Performance goals may force program specific optimizations of the assembly language
Special purpose or embedded processor programmers
  Special functions and heavy dependence on unique I/O devices can make HLL’s useless
Others?

## Slide 20: PERFORMANCE

## Slide 21: Performance
21
KICT, IIUM
Performance
Performance is the key to understanding underlying motivation for the hardware and its organization
Measure, report, and summarize performance to enable users to make intelligent choices.
Why is some hardware better than others for different programs?
What factors of system performance are hardware related?
How does the machine's instruction set affect performance?

## Slide 22: What is Performance?
22
KICT, IIUM
Performance
Airplane Passengers Range (mi) Speed (mph)
Boeing 737-100 101 630 598
Boeing 747 470 4150 610
BAC/Sud Concorde 132 4000 1350
Douglas DC-8-50 146 8720 544
How much faster is the Concorde compared to the 747?
How much bigger is the Boeing 747 than the Douglas DC-8?
So which of these airplanes has the best performance?!

## Slide 23: Computer Performance
23
KICT, IIUM
Performance
Response Time (elapsed time, latency):
  how long does it take for my job to run?
  how long does it take to execute (start to finish) my job?
  how long do I need to wait for the database query?
Throughput:
  how many jobs can the machine run at once?
  what is the average execution rate?
  how much work is getting done?
If we upgrade a machine with a new processor what do we increase?
If we add a new machine to the lab what do we increase?

## Slide 24: Execution Time
24
KICT, IIUM
Performance
Elapsed Time
  counts everything (disk and memory accesses, waiting for I/O, running other programs, etc.) from start to finish
  elapsed time = CPU time + wait time (I/O, other programs, etc.)
CPU time
  doesn't count waiting for I/O or time spent running other programs
  can be divided into user CPU time and system CPU time (OS calls)
CPU time = user CPU time + system CPU time
 elapsed time = user CPU time + system CPU time + wait time
User CPU time (CPU execution time or, simply, execution time)
  time spent executing the lines of code that are in our program

## Slide 25: Performance Comparison
25
KICT, IIUM
Performance
For some program running on machine X: PerformanceX = 1 / Execution timeX
X is n times faster than Y means: PerformanceX / PerformanceY = n

## Slide 26: Clock Cycles
26
KICT, IIUM
Performance
Machine cycle is used instead of reporting execution time in seconds. In modern computers hardware events progress cycle by cycle: each event, e.g., multiplication, addition, etc., is a sequence of cycles
Clock ticks indicate start and end of cycles:
cycle time = time between ticks = seconds per cycle
clock rate (frequency) = cycles per second (1 Hz. = 1 cycle/sec, 1 MHz. = 106 cycles/sec)
Example: A 200 Mhz. clock has a cycle time
time
cycle
tick
tick

## Slide 27: Performance Equation
27
KICT, IIUM
Performance
So, to improve performance one can either:
  reduce the number of cycles for a program, or
  reduce the clock cycle time, or, equivalently,
  increase the clock rate
equivalently
CPU execution time CPU clock cycles Clock cycle time
for a program for a program
=


## Slide 28: How many cycles are required for a program?
28
KICT, IIUM
Performance
Assume that # of cycles = # of instructions
1st instruction
2nd instruction
3rd instruction
4th
5th
6th
...
This assumption is wrong, because
  Different instructions take different amounts of time (cycles)
  Why…?

## Slide 29: How many cycles are required for a program?
29
KICT, IIUM
Performance
Multiplication takes more time than addition
Floating point operations take longer than integer ones
Accessing memory takes more time than that of registers
Important point: changing the cycle time often changes the number of cycles required for various instructions because it means changing the hardware design.

## Slide 30
KICT, IIUM
Example
30
Performance
Computer A which has a 400Mhz Clock runs in 10 seconds.
We are trying to help a computer designer build a new machine B, that will run this program in 6 seconds.
The designer use new (or perhaps more expensive) technology to substantially increase the clock rate
his increase will affect the rest of the CPU design, causing machine B to require 1.2 times as many clock cycles as machine A for the same program.
What clock rate should we tell the designer to target?

## Slide 31: Terminology
31
KICT, IIUM
Performance
A given program will require:
  some number of instructions (machine instructions)
  some number of cycles
  some number of seconds
We have a vocabulary that relates these quantities:
  cycle time (seconds per cycle)
  clock rate (cycles per second)
  (average) CPI (cycles per instruction)
    a floating point intensive application might have a higher average CPI
  MIPS (millions of instructions per second)
    this would be higher for a program using simple instructions

## Slide 32: Performance Measure
32
KICT, IIUM
Performance
Performance is determined by execution time
Do any of these variables represents equal performance?
  # of cycles to execute program?
  # of instructions in program?
  # of cycles per second?
  average # of cycles per instruction?
  average # of instructions per second?

## Slide 33: Performance Equation
33
KICT, IIUM
Performance
CPU execution time Instruction count average CPI Clock cycle time
for a program for a program
=



## Slide 34: Performance Equation
34
KICT, IIUM
Performance
Example:
If a processor runs at a 20 GHz clock rate, how long does it take for the processor to execute a program with 200 instructions (assuming 1 instruction = 1 clock cycle)?
Clock rate/frequency = 20 G = 20x109
Clock cycle time = 1/ (20x109 ) s
1 instruction = 1 clock cycle, i.e., 1 CPI
Instruction count = 200
Execution time for 200 instructions = 200 x 1 x 1/ (20x109 )
= 10 x 10-9 s = 10 ns

## Slide 35: Factors affecting CPI
35
The performance of the pipeline which is the technique used by all modern processors to execute instructions
The performance of the memory system.
KICT, IIUM

## Slide 36
KICT, IIUM
Summary
36
Performance
Performance is specific to a particular program
  total execution time is a consistent summary of performance
For a given architecture performance increases come from:
  increases in clock rate (without adverse CPI affects)
  improvements in processor organization that lower CPI
  compiler enhancements that lower CPI and/or instruction count
Pitfall: expecting improvement in one aspect of a machine’s performance to affect the total performance
Execution Time is the BEST !